## Slide 1: Secure BLE
Ana Pandza
Marin Peko

## Slide 2: GOALS
Establishment of secure communication between Arduino Uno microcontroller and Android application over Bluetooth Low Energy
Speed and efficiency of cryptographic functions on Arduino Uno microcontroller
Applications in many real-world problems

## Slide 3: SECURE COMMUNICATION
PRIVACY
AUTHENTICATION

## Slide 4: PRIVACY
Elliptic-Curve Diffie-Hellman key exchange protocol
Public key
Public key
Compute
Compute
Communication

## Slide 5
AUTHENTICATION
Station-to-Station protocol
Symmetric key
K
is derived from
shared secret
Symmetric key
K
is derived from
shared secret

## Slide 6
STATE_START
STATE_KEYS_GENERATION
STATE_SIGNATURE_VERIFICATION
STATE_ENCRYPTED_CONNECTION
EVENT_CONNECT_REQ
EVENT_PU_KEY_RECEIVED
EVENT_RESET
EVENT_SHARED_SECRET_FAILURE
STATE MACHINE
STATE_SHARED_SECRET_GENERATION
EVENT_ENCRYPTED_SIGNATURE_RECEIVED
EVENT_SIGNATURE_VERIFIED
EVENT_SIGNATURE_NOT_VERIFIED
EVENT_DATA

## Slide 7
MESSAGES
$<MESSAGE_TYPE>=<MESSAGE_CONTENT>;
CONNECT
PU
FAILURE
SIGNVER
SIG
DATA
SIGVER
RESET

## Slide 8
ARDUINO UNO
C / C++
Platformio IDE
VS Code
Classes
MessageParser
StateMachine
ECDHKeyExchange
STS
Specifications | 
Microcontroller | ATmega328P
Flash Memory | 32 KB
SRAM | 2 KB
EEPROM | 1 KB
Clock Speed | 16 MHz

## Slide 9
PERFORMANCES
Operation | Time
Generating ECDH key pair | 3259 ms
Generating shared secret | 3241 ms
AES256 key setup | 437 us
AES256 encryption (per byte) | 24 us
AES256 decryption (per byte) | 46 us
SHA256 hashing | 2835 us

## Slide 10
ANDROID APPLICATION
C#
Xamarin Forms
Visual Studio IDE
  User flow
  enable Bluetooth
  scan for nearby devices
  choose one of the devices
  services and characteristics are listed
  choose characteristic responsible for exchanging messages

## Slide 11
DEMO

## Slide 12
Q & A
?